## Slide 1
EMBEDDED SYSTEMS PROJECT
Smart Density-Based
Traffic Control System
Using IR Sensors and Adaptive Signal Scheduling
Nishit Gupta (24BEC034) | Riti Joshi (24BCS120) | Namita Wayal (24BCS081)
Submitted to: Prof. Sibasankar Padhy • Academic Year 2024–2025

## Slide 2
THE PROBLEM
!
Fixed Signal Timers
Traditional systems use rigid, pre-programmed cycles that never change regardless of actual traffic conditions.
!
Off-Peak Waste
During low-traffic hours, signals still follow the same fixed pattern, causing unnecessary idling and fuel waste.
!
Peak-Hour Backlog
Dense lanes are forced to wait their turn, creating severe congestion while lighter lanes get equal green time.
Conventional traffic signals fail to adapt — causing urban congestion, delays, and inefficiency.

## Slide 3
OBJECTIVES & OVERVIEW
01
Adaptive signal system responding to real-time vehicle density
02
Two-sensor setup per lane to detect queue level and arrival rate
03
Priority score algorithm for fair green signal time allocation
04
Waiting time factor ensures no lane is indefinitely starved
05
16×2 LCD display for live system status and monitoring
06
Correct Red → Green → Yellow transition sequence for safety

## Slide 4
COMPONENTS USED
×1
Microcontroller
(Arduino / 8051)
Central processing & control unit
×6
IR Sensors
2 per lane — detect vehicle presence and arrival (S1 near, S2 far)
×9
LEDs
(R / Y / G)
3 per lane represent Red, Yellow, Green signal lights
×1
16×2 LCD
Display
Real-time status: active lane, countdown, density, next lane
×1
Breadboard
/ PCB
Circuit assembly platform
×1
Power Supply
5V DC
Powers microcontroller and all peripherals

## Slide 5
SYSTEM ARCHITECTURE
Queue Level Detection (S1 + S2 Sensor States)
S1 (Near) | S2 (Far) | Queue Level | Interpretation
0 | 0 | 0 | No vehicles in the lane
1 | 0 | 1 | Small queue near the signal
1 | 1 | 2 | Long queue extending backward
Arrival Rate
Vehicles at S2 ÷ Time Window (10s)
Higher rate = lane filling fast
Waiting Time
Time since last green signal
Resets to 0 when lane gets green turn
Three lanes (L1, L2, L3) each have a near sensor (S1) and a far sensor (S2). Sensor readings are binary — logic 1 = vehicle detected.
L1
S2
S1
L2
S2
S1
L3
S2
S1
← FAR • S2 (Arrival Rate)
S1 (Queue) • NEAR →

## Slide 6
PRIORITY SCORE ALGORITHM
Priority Score = (Queue Level × 5) + (Arrival Rate × 2) + Waiting Time ×2
Queue Level
× 5
Highest priority — clear waiting vehicles first
Arrival Rate
× 2
Anticipate congestion before it builds up
Waiting Time
× 1
Fairness — prevents indefinite lane starvation
Example Calculation
Lane | Queue Level | Arrival Rate | Wait (s) | Score
L1 | 2 | 0.5 v/s | 15 | 26.0
L2 ★ | 1 | 0.8 v/s | 40 | 46.6
L3 | 2 | 0.3 v/s | 20 | 30.6
★ L2 wins despite lower queue — its long wait time elevated the score. Fairness in action!
Dynamic Green Time
Queue 0 → 10 seconds Queue 1 → 15 seconds Queue 2 → 20 seconds

## Slide 7
SIGNAL TRANSITION & OPERATION CYCLE
1
GREEN Phase
Selected lane gets green.
Vehicles pass for the
dynamic green duration.
→
2
YELLOW Phase
Green switches to yellow
for 2–3 seconds to warn
drivers of change.
→
3
ALL-RED Phase
All lanes show red for
1–2 s to clear the
intersection safely.
→
4
NEXT CYCLE
System recalculates
priority scores and
selects the next lane.
1. Read sensors | 2. Compute queue levels | 3. Calc arrival rates | 4. Update wait timers | 5. Compute scores | 6. Select highest | 7. Assign green time | 8. Yellow → All-Red | 9. Reset timer → Repeat

## Slide 8
16×2 LCD DISPLAY INTERFACE
Screen 1 — Signal Status
LN:B T:12
Q 0 2 1
LN:B = Lane B active | T:12s remaining | Q = density per lane
Startup Screen
SMART TRAFFIC
Shown for 2 seconds on power-on
Displays active lane and countdown timer
Shows traffic density (Q-level) for all 3 lanes
Cycles between screens every 3–4 seconds
Switches to transition screen during signal changes
Startup splash screen on power-on

## Slide 9
RESULTS & OBSERVATIONS
✓
Priority scoring correctly identified the most congested lane in all test cases
✓
Dynamic green time allocation reduced unnecessary waiting for low-density lanes
✓
Waiting time component prevented repeated lane skipping — fairness maintained
✓
Yellow and all-red phases executed correctly — no simultaneous green across lanes
✓
LCD displayed active lane, countdown, queue levels, and next lane accurately
✓
Arrival rate detection via S2 allowed anticipation of growing congestion

## Slide 10
SMART vs CONVENTIONAL SYSTEMS
Feature | Conventional System | Proposed Smart System
Signal Timing | Fixed, pre-programmed | Dynamic, real-time data
Congestion Handling | Ignores actual traffic density | Prioritises denser lanes automatically
Fairness | Rigid round-robin | Weighted score with waiting time factor
Starvation Prevention | Not guaranteed | Built into the priority formula
Hardware Complexity | Simple timers only | Sensors + microcontroller logic
Display Feedback | None | 16×2 LCD with live data
The adaptive system outperforms conventional signals across every dimension — efficiency, fairness, and transparency.

## Slide 11
LIMITATIONS & FUTURE SCOPE
Current Limitations
IR sensors assume single-lane; cannot count vehicles in multi-lane wide roads
No pedestrian signals or emergency vehicle priority override
Environmental factors (rain, dust, bright light) may affect IR accuracy
Fixed arrival rate window may not adapt well to sudden traffic bursts
Future Enhancements
Camera-based computer vision for accurate vehicle counting across lanes
Emergency vehicle detection module (ambulance / fire truck override)
IoT connectivity for city-wide adaptive traffic coordination
Machine learning on historical patterns for preemptive signal adjustment
Pedestrian push-button integration for safe road-crossing

## Slide 12
CONCLUSION
The Smart Density-Based Traffic Control System demonstrates that a low-cost, adaptive traffic management solution can be built using IR sensors and a microcontroller.
Replaces fixed-time cycles with a congestion score-driven algorithm
Combines queue level, arrival rate, and waiting time for fair signal allocation
Heavily congested lanes are cleared first; lighter lanes guaranteed service
LCD interface makes decision-making transparent for live demonstration
Solid foundation for smart city traffic management solutions
Nishit Gupta • Riti Joshi • Namita Wayal | Embedded Systems, 2024–25